## Slide 1: A 130 nm Sub-VT Power-Gated Processor for Body Sensor Network Applications
Yanqing Zhang
Yousef Shakhsheer
4/22/2010

## Slide 2: Motivation
Reduce leakage power through power gating
Automate design flow
Contribute to the UVA infrastructure

## Slide 3: Header Switches
Need to be big enough not to degrade performance
Need to be big enough to reduce power gating recovery overhead
Need to be as small as possible to reduce leakage

## Slide 4: Completed Tasks
Looked into CPF
Synthesized two registers with power constraints
Design has been placed and routed
Ran characterization on power gated and normal cells

## Slide 5: Our Design

## Slide 6: CPF
# Technology part of the CPF
# define the isolation, always-on, and retention cells
# define the power switch cells
define_power_switch_cell -cells "HDX2 HDX4 HDX8 HDX16 HDX32 HDX64" \
-stage_1_enable !_EN -type header -gate_bias_pin gnd -power_switchable VDDS -power vdd \
-on_resistance 100.0
# Design part of the CPF
# create power domains
create_power_domain -name PD1 -default
create_power_domain -name PD2 -instances {REG_1} \
-shutoff_condition {enable} -secondary_domains PD1
# create nominal conditions
create_nominal_condition -name off -voltage 0
create_nominal_condition -name on -voltage 0.4
# create power modes
create_power_mode -name PM1 -domain_conditions {PD1@on PD2@on} -default
create_power_mode -name PM2 -domain_conditions {PD1@on PD2@off}
# create rules for isolation logic insertion
# create rules for state retention insertion
# create rules for power switch insertion
create_power_nets -nets vdd -voltage 0.4
create_power_switch_rule -name SW1 -domain PD2 -external_power_net vdd
# specify power targets
#set_power_target -leakage 30 -dynamic 250
# update the rules with implementation info
#update_isolation_rules -names iso1 -location to -cells ISOLNX2M
#update_isolation_rules -names iso2 -location to -cells ISOLNX2M
update_power_switch_rule -name SW1 -cells "HDX2 HDX4 HDX8 HDX16 HDX32 HDX64" -enable_condition_1 !enable -prefix CDN_ -average_ir_drop_limit 0.020 -peak_ir_drop_limit 0.040
# Additional Information for Physical Implementation
# declare power and ground nets
create_power_nets -nets VDDS -internal -average_ir_drop_limit 0.020 -peak_ir_drop_limit 0.040
create_ground_nets -nets gnd -voltage 0
# (optional) create global connections
create_global_connection -net vdd -pins vdd
create_global_connection -net gnd -pins gnd
# add implementation info for power domains
update_power_domain -name PD1 -primary_power_net vdd -primary_ground_net gnd
update_power_domain -name PD2 -primary_power_net VDDS -primary_ground_net gnd -transition_cycles 2.0
update_power_mode -name PM2 -average_ir_drop_limit PD2@0.020 -peak_ir_drop_limit PD2@0.040

## Slide 7: To Do
Power gate PIC processor
Continue to refine automated process